## Slide 1: 60 GHz Flyways: Adding multi-Gbps wireless links to data centers
Daniel Halperin
Srikanth Kandula, Jitu Padhye Victor Bahl, David Wetherall

## Slide 2: Today’s data center networks are oversubscribed in the core
Perform well in average case with job placement
Bottlenecks in core can be workload “hotspots”
…
…

## Slide 3: Eliminating oversubscription is expensive
No core hotspots
No job placement
Costly switches
Complex wiring
…
…

## Slide 4: Our goal: Flyways
To enable a network with an oversubscribed core to act like a non-oversubscribed network by dynamically injecting high-bandwidth links.

## Slide 5: Our approach: Wireless Flyways
Low cost
Perform well in most cases with job placement
Dynamically inject links where needed
…
Oversubscribed Core

## Slide 6: System overview
DC Scheduler
Jobs
Data placement
Flyway Controller
Demands

## Slide 7: Outline of the rest of this talk
60 GHz wireless technology
Wireless flyways system design
Evaluation on real data center workloads

## Slide 8: 60 GHz Wireless

## Slide 9: 60 GHz primer
7 GHz of unlicensed spectrum @60 GHz
Forthcoming IEEE 802.11ad: 3 channels, bitrates to 6.76 Gbps
Challenge:
  60 GHz link has 55 dB (312,000x) worse SNR than 2.4 GHz link
  Directionality is a fundamental mechanism to enable 60 GHz communication
2.4 GHz
5 GHz
60 GHz

## Slide 10: Directionality is crucial
Goodput (Gbps)
1
2
3
0
4
0 5 10 15 20
Distance (m)

## Slide 11: 60 GHz directional technology
Phased Array
Compact (1 in2)
Electronic steering (µs)
Physical Antenna
Fixed position

## Slide 12: 60 GHz for Flyways
60 GHz links
Multi-Gbps
Directional
Steerable
Flyways must be
Reliable
Densely deployed

## Slide 13: Directional 60 GHz links are not robust to blockage
Beam Interrupted
SNR (dB)
Time (s)
30
15
0

## Slide 14: A 60 GHz link in a data center

## Slide 15: Directional 60 GHz links are stable in a data center
24h in Data Center
Time (h)
SNR (dB)
40
20
0
Beam Interrupted
SNR (dB)
Time (s)
30
15
0

## Slide 16: Measurement-based 802.11ad simulator
Simulator to evaluate many concurrent flyways
  Channel model from indoor/DC RF measurements
  Measured 60 GHz antenna patterns
  Also compared to 8-element 2.4 GHz “Phocus” array
Implementation in ns-3
  802.11ad physical layer and protocol
  TCP and UDP packet simulations
  Dozens of concurrent multi-Gigabit links

## Slide 17: Flyways can be densely deployed
160 racks, based on real DC topology
Draw random links until no more can be added
Ensure all links meet rate threshold
12-30 links per channel, depending on rate
# Concurrent links per channel
Omni
Wide
Phocus
Narrow

## Slide 18: Measurement summary
60 GHz offers multi-Gbps, directional, steerable wireless links with IEEE 802.11ad
Measurements and simulations show
  Links are reliable in data centers
  With directionality, links can be densely deployed
Many additional measurements in paper

## Slide 19: Wireless Flyways System Design

## Slide 20: System overview
DC Scheduler
Jobs
Data placement
Flyway Controller
Demands

## Slide 21: Flyway controller architecture
Traffic
Demands
Wireless links & Rates
Compute optimal Flyways set
Configure flyways

## Slide 22: Flyway controller architecture
Traffic
Demands
Wireless links & Rates
Iteratively choose best flyway
Update
Configure flyways
More?
Y
N

## Slide 23: Flyway controller architecture
How to setup links, predict bitrates, and manage interference
How to select flyways that will improve performance
Wireless links & Rates
Iteratively choose best flyway

## Slide 24: Coordinating devices
Leverage the wired backbone to sidestep issues of coordination
✘

## Slide 25: Orienting antennas
Traditional algorithms search, e.g. sector sweep
Data center topology is known and stable

## Slide 26: Predicting bitrate
This is hard in multi-path environments
Directionality alleviates
multi-path: SNR lookup table
[DIRC, SIGCOMM’09]
Use SINR for interference

## Slide 27: High-efficiency MAC
Offload small reverse TCP packets to wired network:
+25% wireless goodput

## Slide 28: Flyway controller architecture
How to setup links, predict bitrates, and manage interference
How to select flyways that will improve performance
Iteratively choose best flyway
Wireless links & Rates

## Slide 29: Selecting flyways: Simple example
Base 10 Gbps network:
15 seconds
S1
D
S3
S2
40
Gb
60
Gb
50
Gb

## Slide 30: “Straggler”: Flyway at largest hotspot
S2
Base 10 Gbps network:
15 seconds
Straggler:
12.2 seconds
S1
D
S3
3 Gbps
40
Gb
60
Gb
50
Gb

## Slide 31: “Transit”: Forward traffic on flyway
S2
Base 10 Gbps network:
15 seconds
Straggler:
12.2 seconds
Transit:
11.7 seconds
S1
D
3 Gbps
S3
40
Gb
60
Gb
50
Gb

## Slide 32: “Greedy”: Choose faster flyways
S2
S3
40
Gb
60
Gb
50
Gb
Base 10 Gbps network:
15 seconds
Straggler:
12.2 seconds
Transit:
11.7 seconds
Greedy:
9.4 seconds
S1
D
6 Gbps

## Slide 33: Flyway controller architecture
Traffic
Demands
Wireless links & Rates
Iteratively choose best flyway
Update
Configure flyways
More?
Y
N

## Slide 34: Evaluation

## Slide 35: Evaluation using real DC workloads
We studied four live data centers
  Mix of applications (Cosmos, IndexSrv, 2xHPC)
  Pre-production and production servers
76 hours of traces, 114 TB of traffic
  Measured application demand

## Slide 36: Traffic matrix example
Source Rack
Destination Rack
Demand
Hypothetical demand
matrix needs full-bisection

## Slide 37: Real traces have localized hotspots
Very few hotspots!
Source Rack
Destination Rack
Affect only a few racks

## Slide 38: Evaluation setup
Evaluated 60 GHz flyways improvements on real demand matrices in an ns-3 topology based on real DC layout
Metric: Completion time of Demands (CTD)
  Relative to non-oversubscribed network
  CTD of 1 ➠ same as non-oversubscribed
  CTD of 2 ➠ same as 1:2 oversubscribed

## Slide 39: 1 flyway device / node
CDF
over
Demand
Matrices
CTD
CTD < 1.5 for >80% of traces
Smallest possible CTD for 50% of traces
1
1.5
2

## Slide 40: Incremental benefit of strategies
CTD
1.5
2
CDF
over
Demand
Matrices
1

## Slide 41: 1-3 devices / node
CTD
1.5
2
CDF
over
Demand
Matrices
1

## Slide 42: Conclusions
60 GHz flyways can substantially improve performance in oversubscribed DC
Traffic indirection crucial for practical benefit in real workloads
Novel techniques leverage wired backbone to dramatically simplify and speed hybrid system
Read more: http://r.halper.in/paper/flyways_sigcomm11